## Slide 1: Beginning Raspberry Pi

## Slide 2: Contents
Raspberry Pi
Installing Raspbian
Connecting to Raspbian
Configuring Raspbian
Update Raspbian
VNC
Installing apache web server + PHP

## Slide 3: Raspberry Pi
a series of credit card–sized single-board computers
developed in the UK by the Raspberry Pi Foundation
  promoting the teaching of basic computer science
Raspberry Pi 3 Spec.
  Broadcom BCM2837 SoC
    CPU: 1.2GHz quad-core ARM Cortex-A53
    1GB RAM
    GPU: 400MHz VideoCore IV
  4 USB ports, 40 GPIO pins, HDMI, Ethernet, 3.5mm audio jack, Micro SD slot

## Slide 4: Comparison of RPi Series
Source: http://hackaday.com/2016/02/28/introducing-the-raspberry-pi-3/

## Slide 5: Raspberry Pi - OSes
Raspbian – based on Debian
Ubuntu mate
Snappy Ubuntu core
Windows 10 IoT core
OSMC – Open source media center
OpenELEC
Risc OS

## Slide 6: Installing Raspbian
Download the Image of raspbian
  https://www.raspberrypi.org/downloads/raspbian/
Writing the Image to the SD card (micro SD card)
  In Windows
  Win32DiskImager
    http://sourceforge.net/projects/win32diskimager/
From https://www.raspberrypi.org/documentation/installation/installing-images/README.md
* If your SD card is not formatted correctly, use SDFormatter https://www.sdcard.org/downloads/formatter_4/

## Slide 7: Installing Raspbian
Partition of the SD card
boot: files required to boot the raspbian
Raspbian image
Free! You can extend the Raspbian’s partition to this area, or use it for other purposes.

## Slide 8: Enable UART (Serial)
Open boot/config.txt and Add the following to enable serial comm.
  enable_uart = 1
Open boot/cmdline.txt and remove ‘quiet’ directive to display boot messages

## Slide 9: Connecting to Raspbian
Recommended Tools (for Windows)
  Notepad++ (with Hack font (optional)) for Editor
    https://notepad-plus-plus.org/
    http://sourcefoundry.org/hack/
  Putty.exe for SSH client
    http://www.chiark.greenend.org.uk/~sgtatham/putty/download.html
  TightVNC Viewer for VNC client
    http://www.tightvnc.com/
    Installation guide: https://www.raspberrypi.org/documentation/remote-access/vnc/windows.md
Insert the SD card to Raspberry Pi 2/3/zero

## Slide 10: Connecting to Raspbian
Connecting Raspberry pi to PC through USB2Serial Cable(Adafruit 954)
  https://www.adafruit.com/products/954
  Cable connection
USB to Serial cable device driver (PL2303)
  https://www.adafruit.com/images/product-files/954/PL2303_Prolific_DriverInstaller_v1_12_0.zip
More information - http://elinux.org/RPi_Serial_Connection
Raspberry pi 2’s GPIO | USB2serial cable
GND | GND (black)
TXD0 | RXD (white)
RXD0 | TXD (green)
5V0 | VCC (red) - optional (power from serial)

## Slide 11: Connecting to Raspbian

## Slide 12: Connecting to Raspbian
Check the PORT number of the cable in device management
Use putty.exe to connect the Raspberry pi via COM port

## Slide 13: Connecting to Raspbian
putty
Connection type: Serial
Serial Line: COM?
Speed: 115200

## Slide 14: Connecting to Raspbian
ID: pi
Password: raspberry

## Slide 15: Configuring Raspbian
Raspi-config
  $ sudo raspi-config
Expand Filesystem
  Use all of the SD card for Raspbian
  Check the size of the partition using ‘df’ command
sudo?
Run program with super user’s privileges.

## Slide 16: Configuring Raspbian
Wireless configuration
  $ sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
$ sudo reboot
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
network={
ssid="hswlan"
scan_ssid=1
key_mgmt=WPA-EAP
identity="학번/사번"
password="비밀번호"
}

## Slide 17: Configuring Raspbian
ifconfig wlan0
netstat -nr

## Slide 18: Update Raspbian
$ sudo apt-get update
  To update the local package index with the latest changes made in the repositories (/etc/apt/sources.list)
$ sudo apt-get upgrade
  Upgrade all installed packages

## Slide 19: VNC (Virtual Network Computing)
Graphical desktop sharing system that allows you to remotely control the desktop interface
Install the TightVNC package
  $ sudo apt-get install tightvncserver
Rrun TightVNC Server
  $ tightvncserver
  will prompt you to enter password
Run VNC server
  $ vncserver :1 -geometry 1024x768 -depth 24
From https://www.raspberrypi.org/documentation/remote-access/vnc/

## Slide 20: VNC (Virtual Network Computing)
Connecting VNC
Run TightVNC Viewer in your PC (windows)

## Slide 21: VNC (Virtual Network Computing)
Listening port 80 (HTTP) only allowed in Our Site.
But, normal pi user cannot listen 80 port.
We need to forward other port to 80 port.
  $ sudo iptables -t nat -A PREROUTING -p tcp --dport 80 -j REDIRECT --to 5901
  This forward 80 to 5901
Run VNC server
  $ vncserver :1 -geometry 1024x768 -depth 24
  vncserver will listen at port 5901
if you want to delete the forwarding in the iptable:
$ sudo iptables -t nat -D PREROUTING -p tcp --dport 80 -j REDIRECT --to 5901

## Slide 22: VNC (Virtual Network Computing)
Connect to the port 80 of the raspberry pi
Remote Host: 223.194.131.30::80

## Slide 23: VNC (Virtual Network Computing)

## Slide 24: Installing Web Server
$ sudo apt-get install apache2
/var/www/html/index.html
$ sudo nano /var/www/html/index.html
  Modify the HTML

## Slide 25: Installing PHP
$ sudo apt-get install php5 libapache2-mod-php5
$ sudo nano /var/www/html/index.php
<?php
echo “Hello world”;
phpinfo();
?>

## Slide 26: Q&A